## Slide 1
NETWORK DESIGN &
IMPLEMENTATION REPORT
A Comprehensive LAN Architecture for a Small-to-Medium Enterprise
Limkokwing University of Creative Technology | Information Technology | DCOMP 114

## Slide 2
CONTENTS
Network Design
Implementation Report
01
Executive Summary & Objectives
02
OSI and TCP/IP Theoretical Framework
03
LAN Fundamentals & Ethernet
04
Network Topology Design
05
Switching Technologies & L2 Protocols
06
IPv4 Addressing & Subnetting
07
Layer 3 Routing Principles
08
Wireless Networking & NAT Security
09
Troubleshooting & Verification
10
Conclusion & Future Scalability

## Slide 3
01 EXECUTIVE SUMMARY
3
Subnets
4
Routing Phases
254
Hosts/Subnet
100%
Uptime Goal
Designed and simulated a scalable LAN for a small-to-medium enterprise using Cisco Packet Tracer.
Implemented hierarchical star topology with a Core Router (Router0), two Cisco 2960 switches, and a Linksys WRT300N wireless router.
Network guarantees collision-free traffic via Layer 2 switching, with Layer 3 inter-departmental routing.
Integrated wireless mobility via IEEE 802.11 with NAT security sandboxing for mobile clients.
Rigorous multi-phase testing (ping, ARP, ICMP) confirmed 100% cross-subnet connectivity.

## Slide 4
02 OSI & TCP/IP MODELS
7
Application
User-facing protocols (HTTP, FTP, DNS)
6
Presentation
Encryption, encoding, compression
5
Session
Session management & synchronization
4
Transport
TCP/UDP – reliable or fast delivery
3
Network
IP addressing & routing (Router0)
2
Data Link
MAC frames, Cisco 2960 switching
1
Physical
Copper cables, RF signals, hardware
TCP/IP MODEL
Application
Transport
Internet
Network Access

## Slide 5
03 LAN FUNDAMENTALS & ETHERNET
IEEE 802.3 Ethernet
FastEthernet (100 Mbps) and GigabitEthernet (1 Gbps) interfaces used for high throughput and low latency throughout the topology.
Collision Domains
Each switch port = isolated collision domain. Full-duplex communication enabled. No packet collisions between PC0 and PC1 on SW1.
Broadcast Domains
The Core Router segments Dept A (SW1) and Dept B (SW2) into separate broadcast domains — preventing ARP storms from crossing subnets.
Client-Server Model
Server0 (192.168.10.100) provides centralized resources. The router ensures Dept B (20.x) and wireless (0.x) users can reach it.

## Slide 6
04 NETWORK TOPOLOGY DESIGN
Segment 1
Core Infrastructure & Admin
192.168.10.0 /24
Core Router Gig0/0 → .1
Server0 → .100
PC0, PC1, PC2 → .11+
Segment 2
General Operations (Dept B)
192.168.20.0 /24
Core Router Gig0/1 → .1
PC3, PC4, PC5 → .10, .11, .12
ACL-ready for future security
Segment 3
Wireless & Mobile Access
192.168.30.x + 192.168.0.x
Transit link → .30.2
Linksys DHCP pool → .0.x
PC6, PC7 via Wi-Fi + NAT
Hierarchical Star Topology · Cisco 2960 Switches · Fault-isolated segments

## Slide 7
05 SWITCHING TECHNOLOGIES & LAYER 2 PROTOCOLS
Cisco Catalyst 2960
Switch
CAM
CAM / MAC Table
Switch builds a MAC address table on startup. Maps port → MAC. After population, frames are forwarded only to the correct port.
FWD
Frame Forwarding
Known MAC = unicast forward. Unknown MAC or broadcast (FF:FF:FF:FF:FF:FF) = flood to all ports except source.
ARP
ARP & First Timeout
First inter-subnet ping times out while the router sends ARP. Subsequent packets succeed with TTL=127, ~10 ms latency.
STP
Spanning Tree (STP)
IEEE 802.1D prevents bridging loops. Amber cable indicator in Packet Tracer = STP convergence in progress.

## Slide 8
06 IPv4 ADDRESSING & SUBNETTING
Device
Interface
IP Address
Subnet
Gateway
Core Router
Gig0/0
192.168.10.1
/24
N/A
Core Router
Gig0/1
192.168.20.1
/24
N/A
Core Router
Gig0/2
192.168.30.1
/24
N/A
Server0
Fa0
192.168.10.100
/24
192.168.10.1
PC0-PC2
Fa0
192.168.10.x
/24
192.168.10.1
PC3-PC5
Fa0
192.168.20.x
/24
192.168.20.1
Wireless Router
WAN
192.168.30.2
/24
192.168.30.1
Wireless Router
LAN
192.168.0.1
/24
N/A
PC6, PC7 Wi-Fi
Wireless0
192.168.0.x
/24
192.168.0.1
Class C Private Range 192.168.0.0 – 192.168.255.255 | RFC 1918 | 254 usable hosts per /24

## Slide 9
07 LAYER 3 ROUTING PRINCIPLES
Core Router (Router0)
Cisco IOS
Hardware ASIC
01
Default Gateway Check
PC0 (10.3) compares PC3 (20.10) against its /24 mask — different network. Sends frame to gateway 192.168.10.1.
02
Decapsulation at Router
Router receives Ethernet frame, strips L2 header, examines inner IP packet. Destination = 192.168.20.10.
03
Routing Table Lookup
Router checks Connected routes. 192.168.20.0 → Gig0/1. No dynamic routing needed — directly connected.
04
Re-encapsulation & Forward
New Ethernet frame: Src MAC = Gig0/1, Dst MAC = PC3. Fired out Gig0/1 → SW2 → PC3. Reply reverses the process.

## Slide 10
08 WIRELESS NETWORKING & NAT SECURITY
Linksys WRT300N
IEEE 802.11 Wireless Router
Standard:
IEEE 802.11 (2.4 GHz / 5 GHz)
Medium:
Radio Frequency (RF)
CSMA/CA:
Collision Avoidance Protocol
Security:
WPA2 / AES Encryption (PSK)
DHCP Pool:
192.168.0.100 → .254
WAN IP:
192.168.30.2 (from Core Router)
LAN GW:
192.168.0.1 (internal)
NAT / PAT Flow
① PC6 (192.168.0.102) sends ping to Server0 (192.168.10.100)
② Linksys translates Src IP → 192.168.30.2 (WAN IP). Records in NAT table.
③ Core Router routes packet as if from 192.168.30.2. Server0 replies.
④ Linksys receives reply, consults NAT table, translates Dst back → 192.168.0.102.
⑤ Result: Wireless clients are securely sandboxed. External devices cannot initiate inbound connections.

## Slide 11
09 TROUBLESHOOTING & FINAL VERIFICATION
Phase 1
Local Subnet Test
PC0 → PC1 (both 192.168.10.x). Tests L1 cabling, L2 switching on SW1, local IPv4. Result: 4/4 packets ✓
Phase 2
Default Gateway Test
PC0 → 192.168.10.1 (Core Router Gig0/0). Verifies switch-to-router trunk link. Result: 100% success ✓
Phase 3
Cross-Subnet (L3) Test
PC0 → PC3 (192.168.20.10). First packet timeout (ARP cache empty). Packets 2-4: TTL=127, ~10ms ✓
Phase 4
Wireless-to-Wired Test
PC6 (Wi-Fi) → Server0 (192.168.10.100). NAT translation, DHCP assignment, full ICMP reply chain. ✓

## Slide 12
10 CONCLUSION & FUTURE SCALABILITY
Key Achievements
✓ Hierarchical star topology with full fault isolation per segment
✓ Class C /24 subnets — 254 hosts each, ready for future expansion
✓ Cisco 2960 hardware switching eliminates collisions at wire speed
✓ Inter-subnet routing via directly-connected routes (no dynamic routing needed)
✓ NAT security sandbox fully isolates wireless mobile clients
✓ All 4 test phases passed — 100% end-to-end connectivity verified
Future Scalability
→ Add switches uplinked to SW1/SW2 — no re-IP needed
→ Implement VLANs on Cisco 2960 for micro-segmentation
→ Deploy ACLs on Core Router to restrict cross-subnet access
→ Add OSPF/EIGRP if additional routers are introduced
→ Upgrade WPA2 → WPA3 for enhanced wireless security
→ Introduce redundant links & HSRP for high availability
Limkokwing University of Creative Technology | DCOMP 114 | Network Administration